## Slide 1: NetAcad Modules 3-7 Review

## Slide 2: IP Addressing
ITN Chapter 7
3

## Slide 3: IP Terminology
Dotted-decimal notation: an IP address written in 4 octets in decimal format
Binary: base 2 number system of 0s and 1s
Octet: a group of 8 binary digits
Network portion: bits of the IP address that identify the subnet
Host portion: bits of the IP address that identify individual nodes
Subnet mask: used to identify the network and host portions of an address
Prefix length: (also known as slash or CIDR notation) the number of 1s in the binary form of the subnet mask

## Slide 4: Addressing Terminology
Static IP address: an IP address manually managed by an administrator or user
Dynamic IP address: an IP address automatically managed by a server
Unicast: communication between two individual devices
Multicast: a message sent from one device to a group of devices
Broadcast: a message sent from one device to all listening devices
Public address: can be used globally
Private address: can only be used within an internal network

## Slide 5: Private Addresses
10.0.0.0/8
or 10.0.0.0 to 10.255.255.255
172.16.0.0/12
or 172.16.0.0 to 172.31.255.255
192.168.0.0/16
or 192.168.0.0 to 192.168.255.255

## Slide 6: Classful Addressing
Legacy addressing where networks are assigned a network address in a class with a predefined allowed number of hosts
Replaced with CIDR addressing to allow for less waste in address allocation

## Slide 7: Subnetting IP Networks
ITN Chapter 8
4

## Slide 8: Subnetting Terminology
Subnet: section of a network
Broadcast domain: group of devices that can receive a broadcast from one another; usually all connected by layer 2 switches in one subnet
Octet boundary: subnet created using a /8, /16, or /24 subnet mask
VLSM: (Variable Length Subnet Mask) dividing a network into subnets of different sizes in order to conserve address space

## Slide 9: Planning a Network
Broadcast domains must remain manageable
Must leave enough possible subnets for future expansion
Each subnet must have enough possible host addresses for future expansion
/24 is the most common subnet boundary as it allows for many different subnets with up to 254 hosts
Most devices should have a dynamically allocated IP, whereas servers and network devices should have a static IP
Conserving address space is not much of a concern in IPv6, so networks do not need as detailed planning as IPv4

## Slide 10: Classless Subnetting
Bits are “borrowed” from the host portions to create subnets of the original network
Ex. 192.168.0.0/16 is the network address and 8 bits are borrowed via a /24 subnet mask
  There can be 254 subnets with 254 hosts each
  One subnet could be 192.168.10.0 and a host on that subnet could be 192.168.10.1
  Broadcast address of that subnet is 192.168.10.255
Subnets should be chosen based on the number of needed hosts to conserve addressing space

## Slide 11: Example Subnets